## Slide 1: Heart Sound Classification Using LSTM
Maryam Eskandari

## Slide 2: Introduction
Heart auscultation: the primary tool for screening and diagnosis in primary health care
Stethoscopes to capture heart sound
Heart sound as PhonoCardioGram (PCG) data for diagnostic purposes
Goal: Diagnose murmur from normal heart sound

## Slide 3: Data
One or more heart sound recordings for 1568 patients from auscultation locations
Pulmonary valve (PV),
Aortic valve (AV),
Mitral valve (MV),
Tricuspid valve (TV),
And other (Phc)
The recordings were collected sequentially (not simultaneously) from different auscultation locations using a digital stethoscope.
The number, location, and duration of the recordings vary between patients.

## Slide 4: Data Preprocessing
PCG data were originally sampled to 4000 Hz
Each PCG was resampled to 1000 Hz
To reduce the data size
It also maintain useful information
Band-pass filtered between 25 Hz and 400 Hz
0-100 Hz,
100-200 Hz,
200-300 Hz,
300-400 Hz.
And then pre-processed to remove any spikes in the PCG

## Slide 5: Data Preprocessing
There are 5 recordings per patients
Min length 7 seconds
Max length>30 seconds
We produced 4 band-pass filters per each channel
Therefore, 20 recording per patient (at most)
For each recording, it is split into windows of 1 second length with 0.5 second overlap

## Slide 7: Approaches
XGBoost over Extracted Features
LSTM over preprocessed signals (signals not extracted features)
BiLSTM over preprocessed signals
GRU over preprocessed signals
Parallel LSTM over preprocessed signals

## Slide 8: Feature extractions
We use two class of features extracted from 20 recordings and multiple windows (LibRosa library were used for feature extraction)
Time Domain Features
Frequency Domain Features

## Slide 9: Time-domain Features
Mean and standard deviation (SD) of the following parameters were used as time-domain features (36 features):
PCG intervals:
  RR intervals,
  S1 intervals,
  S2 intervals,
  systolic intervals,
  diastolic intervals,
  ratio of systolic interval to RR interval of each heart beat,
  ratio of diastolic interval to RR interval of each heart beat,
  ratio of systolic to diastolic interval of each heart beat.

## Slide 10: Time-domain Features (Cont.)
Average and STD of PCG amplitudes:
  ratio of the mean absolute amplitude during systole to that during the S1 period in each heart beat,
  ratio of the mean absolute amplitude during diastole to that during the S2 period in each heart beat,
  skewness of the amplitude during S1 period in each heart beat,
  skewness of the amplitude during S2 period in each heart beat,
  skewness of the amplitude during systole period in each heart beat,
  skewness of the amplitude during diastole period in each heart beat,
  kurtosis of the amplitude during S1 period in each heart beat,
  kurtosis of the amplitude during S2 period in each heart beat,
  kurtosis of the amplitude during systole period in each heart beat,
  kurtosis of the amplitude during diastole period in each heart beat

## Slide 11: Frequency-domain Features
The power spectrum was estimated using a Hamming window and the discrete-time Fourier transform.
The median power across 4 frequency bands was calculated.
Then, the mean of the median power of the 4 frequency bands were used as frequency-domain features.
Additionally, mel-frequency cepstral coefficient (MFCC) were extracted

## Slide 12: Results of XGBoost on extracted features
 | Absent | Present | Unknown
Absent | 100% | 0% | 0%
Present | 81% | 17% | 3%
Unknown | 71% | 14% | 14%
 | Absent | Present | Unknown
Absent | 138 | 0 | 0
Present | 29 | 6 | 1
Unknown | 10 | 2 | 2
Overall Accuracy = 78%

## Slide 13: Training folds as well as validation and test folds for developing five models for murmur detection
Model | Training Folds | Validation Fold | Test Fold
1 | 0,1,2 | 3 | 4
2 | 1,2,3 | 4 | 0
3 | 2,3,4 | 0 | 1
4 | 3,4,0 | 1 | 2
5 | 4,0,1 | 2 | 3
To have a more generalizable model, a stratified 5-fold cross-validation was used.

## Slide 14: Data distribution after stratified 5-fold splitting

## Slide 15: Accuracy on Preprocessed Signals
Test | LSTM | BiLSTM | GRU | Parallel LSTM
Fold 0 | 80 | 81 | 77 | 82
Fold 1 | 79 | 82 | 79 | 80
Fold 2 | 83 | 80 | 81 | 79
Fold 3 | 79 | 78 | 77 | 83
Fold 4 | 80 | 78 | 80 | 81
Average | 80.2 | 79.8 | 78.8 | 81
Chart: Accuracy of different folds using different approaches
| Fold 0 | Fold 1 | Fold 2 | Fold 3 | Fold 4 | Average
LSTM | 80 | 79 | 83 | 79 | 80 | 80.2
BiLSTM | 81 | 82 | 80 | 78 | 78 | 79.8
GRU | 77 | 79 | 81 | 77 | 80 | 78.8
Parallel LSTM | 82 | 80 | 79 | 83 | 81 | 81

## Slide 16: Parallel LSTM vs. XGBoost Fold 4 as test, Fold 3 as Val
 | Absent | Present | Unknown
Absent | 100% | 0% | 0%
Present | 64% | 31% | 6%
Unknown | 57% | 21% | 21%
 | Absent | Present | Unknown
Absent | 100% | 0% | 0%
Present | 81% | 17% | 3%
Unknown | 71% | 14% | 14%
Parallel LSTM
XGBoost
Accuracy: 81%
Accuracy: 78%
Issue: Still biased toward majority class

## Slide 17: Solving biases toward majority class issue
Solution: Using class weights in the custom loss function
Results:
 | Absent | Present | Unknown
Absent | 91% | 9% | 1%
Present | 33% | 61% | 6%
Unknown | 29% | 36% | 36%
 | Absent | Present | Unknown
Absent | 100% | 0% | 0%
Present | 64% | 31% | 6%
Unknown | 57% | 21% | 21%
Parallel LSTM Before
Accuracy: 81%
Parallel LSTM After
Accuracy: 81%
No Change in accuracy but much more balanced results across classes

## Slide 18: Another issue
Data
Data length is too long
Median 21 seconds
4000 hz
Murmur
The murmur can be detected in much smaller frequency (even 500 hz in some studies) too.
Solution
Resample the signals to lower frequency

## Slide 19: Results of parallel LSTM after resampling
Different resampling were tested such as 2000 hz, 1000 hz, 800 hz, 500 hz
800 hz performed the best
 | Absent | Present | Unknown
Absent | 92% | 7% | 1%
Present | 28% | 69% | 3%
Unknown | 43% | 21% | 36%
Parallel LSTM After
Accuracy: 84%

## Slide 20: Thanks